## Slide 1: Logic Gates

## Slide 2: Definition
Logic Gate is a series of Electrical circuit which accepts two or more inputs gives a single output.
There are a total of 7 logic gates. They are:-

## Slide 3: Types of gates
AND Gate
OR Gate
NOT Gate
NAND Gate
NOR Gate
X-OR Gate
X-NOR Gate

## Slide 4: AND Gate
It is an electronic circuit used to perform logical multiplication and is denoted by (.)dot operator. It accepts two or more input & generates only one output
Venn-Diagram
Graphical Symbol
O
A
B
Truth Table Inputs Outputs A B O=A.B 0 0 0 0 1 0 0 0 1 1 1
Boolean Expression
O= A.B
A
B

## Slide 5: OR Gate
It is an electronic circuit used to perform logical addition and is denoted by (+)plus operator. It accepts two or more input & generates only one output
Venn-Diagram
Graphical Symbol
O
A
B
Truth Table Inputs Outputs A B O=A.B 0 0 0 0 1 1 0 1 1 1 1
Boolean Expression
O= A+B
A
B

## Slide 6: NOT Gate
It is an electronic circuit used to perform logical complement and is denoted by (‘)Single quote operator. It accepts one input & generates only one output
Venn-Diagram
Graphical Symbol
O
A
B
Boolean Expression
O= A’
A
A’
Truth Table
Input Output
0 1
1 0

## Slide 7: NAND Gate
It is an electronic circuit used to perform complement of logical multipication and is denoted by (.)dot operator & single quote operator (‘). It accepts two or more input & generates only one output
Venn-Diagram
Graphical Symbol
O
A
B
Truth Table Inputs Outputs A B O= (A.B)’ 0 0 1 0 1 1 0 1 1 1 0
Boolean Expression
O= (A.B)’
A
B

## Slide 8: NOR Gate
It is an electronic circuit used to perform complement of logical addition and is denoted by (+)plus operator & single quote operator (‘). It accepts two or more input & generates only one output.
Venn-Diagram
Graphical Symbol
O
A
B
Truth Table Inputs Outputs A B O= (A.B)’ 0 0 1 0 1 0 0 0 1 1 0
Boolean Expression
O= (A+B)’
A
B

## Slide 9: X-OR Gate
It is an electronic circuit used to perform complement of logical multiplication and is denoted by (.)dot operator & single quote operator (‘). It accepts two or more input & generates only one output
Venn-Diagram
Graphical Symbol
O
A
B
Truth Table Inputs Outputs A B O= (A.B)’ 0 0 1 0 1 1 0 1 1 1 0
Boolean Expression
O= (A.B)’
A
B