## Slide 1: Seeeduino LoRaWAN
Michele La Malva Moreno
Experience LoRa’s advantage
in the field of IoT

## Slide 2: LoRa : Technology
LoRa is the type of radiofrequency modulation patented by Semtech and among its main advantages is:
High tolerance to interference and High sensitivity (-168dB)
Based on FSK modulation
Low consumption
Long range 10 to 20km
Low data transfer (up to 255 bytes)

## Slide 3: LoRaWAN : Protocol
LoRaWAN is a network protocol that uses LoRa technology to communicate and manage LoRa devices, it consists of two parts mainly: gateways and nodes.
Star topology
AES 128 Encryption
Support 3 Types of nodes
Public and Private networks
Device Management

## Slide 4: LoRaWAN : Structure

## Slide 5: LoRaWAN : LoRa mode
In point-to-point connection (P2P) mode, a gateway device is no needed.
Instead, they can transmit information each others directly.
Point-To-Point connection
Mesh structure connection

## Slide 6: LoRaWAN : LoRaWAN OTAA mode

## Slide 7: LoRaWAN : LoRaWAN ABP mode

## Slide 8: LoRaWAN : LoRaWAN OTAA / ABP mode

## Slide 9: Seeeduino LoRaWAN : Board/Processor
ATSAMD21G18 (32-bit ARM Cortex M0+) @ 48MHz with 3.3V logic/power
Embedded with lithium battery management chip and status indicator led
20 GPIOs (All pins but 2 and 7 are PWM)
1 x analog output (10-bit DAC)
6 x analog inputs (12-bit ADC)
4 on-board Grove connectors
3.3V regulator with 200mA output
Flash Memory : 256 kb
SRAM : 32 kb
Device Firmware Upgrade button
Reset button

## Slide 10: Seeeduino LoRaWAN : Board/Modules
RHF76-052AM LoRaWAN module embedded by SX1276 transceiver and MCU STM32L051/052XX.
High link budget of 160dB. -140dBm sensitivity and 19dBm Output power.
Support Class A/C LoRaWAN protocol
1.45uA sleep current in WOR mode
Dual band:
19dBm@434MHz/470MHz
14dBm@868MHz/915MHz
(Optional) GPS Chip L70B-M39

## Slide 11: Seeeduino LoRaWAN : Block Diagram

## Slide 12: Seeeduino LoRaWAN : Block Diagram

## Slide 13: Seeeduino LoRaWAN : In a nutshell
ATSAMD21G18
Processor
Instructions
STM32L051/052XX
SX1276
SRAM, Flash, SERCOM...
AT Commands
SPI
RHF76-52AM module
Gateways, LoRa Devices, etc..

## Slide 14: LoRa in Low-Power Wide-Area Network
ATSAMD21G18
Processor
Instructions
STM32L051/052XX
SX1276
SRAM, Flash, SERCOM...
AT Commands
SPI
RHF76-52AM module
Gateways, LoRa Devices, etc..
ATSAMD21G18
Processor
Instructions
STM32L051/052XX
SX1276
SRAM, Flash, SERCOM...
AT Commands
SPI
RHF76-52AM module
ATSAMD21G18
Processor
Instructions
STM32L051/052XX
SX1276
SRAM, Flash, SERCOM...
AT Commands
SPI
RHF76-52AM module
Star topology

## Slide 15: LoRa in Low-Power Wide-Area Network
Star topology
Point to Point Connection
Seeeduino LoRa
Adafruit Feather 32u4 RFM95 LoRa

## Slide 16: LoRa in LPWAN : Hands-On Example
What’s the value of pin A0?
The value of A0 is X volts
Get A0 value
Print A0 value
What’s your GPS-based position?
My position is LAT/LON
Get GPS position
Print position

## Slide 17: LoRa in LPWAN : Hands-On Example
Master side
Wait for frame
0
Slave side
Init
1
Server is asking me a command
Answer with
desired command
I’m a client
I’m a server
2
Ask an available
device a command
Unknow message
or
it’s not for me
No response from client
(Time out)
3
Client answered successfully
Print the answer

## Slide 18: LoRa in LPWAN : Hands-On Example
NOW LET’S FUN BEGIN!
And remember, If it works don’t touch it …